Tango Integration of Modern 2D Detectors
Yuelong Yu
FS-EC
DESY

---
Outline
- Background
- New hybrid pixel detectors
- Lambda tango integration
  - System layout
  - Detector PC
  - Software
  - Tango servers
  - Data
- Summary and Outlook

---
Background
- Motivation
  - Provide detector with high sensitivity, high resolution,high frame rate and large area
- New detector development
  - 2D detector with small pixel size
    - High resolution and large area
  - Hybrid pixel technology
    - Pixelated sensor and Chip are directly connected
    - Fast read-out speed ( kHz )
  - Direct photon conversion
    - Provide high Quantum Efficiency
  - Adaptable sensor material ( e.g. Si, GaAs, CdTe )
    - Covers different range of X-ray energies

---
New Hybrid pixel detectors
- Lambda
  - Based on the Medipix3 readout chip
  - Single Module:1536 x 512 pixels
  - Support both 12 and 24 bit image modes
  - Maximum frame rate:2000 frames/second with 12 bit mode
  - Maximum data rate for single module : ~2.6 GB/s
  - Multi-module system ( Lambda2M ) available
    - Lambda2M contains 3 lambda single module
- AGIPD 1M
  - Multi-module system ( 16 AGIPD single modules )
  - AGIPD 1M system is designed for European XFEL
  - Maximum data rate: 10GB/s

---
Lambda tango integration – System layout
- Single module system
- Lambda2M system
1 GE
1 GE
Detector
PC
DESY
Data center
10 GE
2x10 GE
1 GE
PC
Detector
10 GE
DESY
Data center
2x10 GE
2x1 GE
PC
10 GE
4x10 GE

---
Lambda tango integration – Detector PC
- Detector PC
  - Dedicated detector PC is used for detector control and data acquisition
  - Dell PowerEdge R620 Server or similar standard
  - Intel(R) Xeon(R) CPU E5-2667 0 @ 2.90GHz X 12 cores
  - RAM: 256 GBytes
  - Hard disk: 4 TBytes
  - 6 X 10 GE NICs
  - 2 X 1 GE NICs

---
Lambda tango integration – Software
- Detector SDK
  - Encapsulate the control and data acquisition in the SDK
  - API for further control system integration or user applications
- Tango integration
  - Based on the detector SDK, a tango device server ( DS ) is implemented
  - DS is used to set parameters and control the behaviors of the detector
  - The device is integrated into the experiment control environment
  - For multiple module system, the master tango device server is used to control the slave tango device server

---
Lambda tango integration – Tango servers
- Single module system
- Lambda2M system
Tango Client
Tango DS
PC
Detector
Tango Master
DS
Tango DS
Tango Master DS
PC
Detector
Tango DS
Tango DS
2 x Tango DS
PC
Tango DS

---
Lambda tango integration – Data
- Data compression
  - CPU based parallel data compression is implemented in the detector SDK
  - Hardware Gzip accelerator ( IBM and Comtech EF Data ) is under study.
- Data format
  - Nexus file format is used for saving the meta data and image data
  - File split option is implemented and each file has a user specified size
- GPFS with NFS
  - The GPFS is exported to detector PC using NFS.
  - Detector writes data into mounted directory
- HiDRA
  - An application based on ZMQ used to copy data from detector PC to data center
  - Tested with Pilatus and AGIPD 1M system

---
Summary and Outlook
- Lambda system has been successfully integrated into tango control system at PETRA3 in DESY
- Both single and multi module system work reliably with full speed ( 2000 fps ) data acquisition
- CPU based parallel compression is implemented for the image data
- Hardware compression accelerator will be used in future
- HiDRA will be used to copy data from detector PC and data center for Lambda system
- ZMQ stream of the image data will be provided by detector SDK in future

---
Thank you