## Slide 1: TANGO New Developments New features
Reynald Bourtembourg

## Slide 2: TANGO 9 New Features
DevEnum Attributes
Forwarded Attributes
Pipes
Dynamic commands
New event types
New Polling Algorithm

## Slide 3: TANGO 9 New Features: DEV_ENUM Attributes
New IDL Tango type: DevEnum (29) ~ C++ enumeration
The enumerated values always start at 0
Values are consecutive
It is transferred on the network as DevShort data type
Attributes like the others (name, properties, polling,.....)
+
The Enum definition ( enum _MyEnum { XX, YY, ..} )
Labels for enum fields ( vector<string> )

## Slide 4: TANGO 9 New Features: DEV_ENUM Attributes
Example using POGO:

## Slide 5: TANGO 9 New Features: DEV_ENUM Attributes
Example using POGO (generated code):

## Slide 6: TANGO 9 New Features: DEV_ENUM Attributes
Example using POGO (generated code):

## Slide 7: TANGO 9 New Features: DEV_ENUM Attributes
ATKPanel

## Slide 8: TANGO 9 New Features: DEV_ENUM Attributes
The enumeration labels can be set dynamically after the attribute creation:
1 void MyDev::init_device()
2 {
3 ...
4
5 Attribute &att = get_device_attr()->get_attr_by_name("TheEnumAtt");
6 MultiAttrProp<DevEnum> multi_prop;
7 att.get_properties(multi_prop);
8
9 multi_prop.enum_labels = {/* your fancy enum labels */}; 10 att.set_properties(multi_prop);
11 ....
12 }

## Slide 9: TANGO 9 New Features: DEV_ENUM Attributes
Setting the attribute value:
1 enum Card points
2 {
3 NORTH = 0,
4 SOUTH,
5 EAST,
6 WEST
7 };
8
9 void MyDev::read_TheEnum(Attribute &att)
{
...
12 points = SOUTH;
13 att.set_value(&points);
14 }

## Slide 10: TANGO 9 New Features: DEV_ENUM Attributes
Setting the attribute value:
1 enum Card points
2 {
3 NORTH = 0,
4 SOUTH,
5 EAST,
6 WEST
7 };
8
9 void MyDev::read_TheEnum(Attribute &att)
{
...
12 points = 1; // SOUTH == 1
13 att.set_value(&points);
14 }

## Slide 11: TANGO 9 New Features: DEV_ENUM Attributes
Usage in a Tango client:
1 DeviceAttribute da = the_dev.read_attribute("TheEnumAtt");
2 Card ca;
3 da >> ca;
1 DeviceAttribute da = the_dev.read_attribute("TheEnumAtt");
2 DevShort sh;
3 da >> sh;
OR

## Slide 12: TANGO 9 New Features: Forwarded Attributes
Forwarded Attribute = device attribute mapping an attribute of a root device.
A forwarded attribute is defined by:
A name
A label to overload the root attribute label
An attribute property __root_att in database to set root attribute name

## Slide 13: TANGO 9 New Features: Forwarded Attributes
A forwarded attribute gets its configuration from its root attribute
It forwards to its root attribute:
Its read / write / write_read requests
Its configuration change
Its event subscription
Its locking behavior

## Slide 14: TANGO 9 New Features: Forwarded Attributes

## Slide 15: TANGO 9 New Features: Forwarded Attributes

## Slide 16: TANGO 9 New Features: Forwarded Attributes

## Slide 17: TANGO 9 New Features: Forwarded Attributes

## Slide 18: TANGO 9 New Features: Forwarded Attributes

## Slide 19: TANGO 9 New Features: Forwarded Attributes

## Slide 20: TANGO 9 New Features: Forwarded Attributes

## Slide 21: TANGO 9 New Features: Forwarded Attributes
__root_att can point to an attribute in another control system ( different TANGO_HOST):
e.g: __root_att=tango://somewhere:20000/my/super/dev/attr

## Slide 22: TANGO 9 New Features: Forwarded Attributes

## Slide 23: TANGO 9 New Features: Forwarded Attributes

## Slide 24: TANGO 9 New Features: Forwarded Attributes

## Slide 25: TANGO 9 New Features: Forwarded Attributes
If the root device is not running, the device will be in ALARM
Error message in Status: ''Forwarded attribute xxx not reachable'‘
It will become reachable again as soon as the root device attribute is exported again

## Slide 26: TANGO 9 New Features: Forwarded Attributes
Current limitations:
Alarm quality factor not reflected in State and Status attributes when the fwd and root attributes are in alarm
Can be created dynamically but works with only one exported device/server
Forwarded events sometimes contain the previous attribute value https://github.com/tango-controls/JTango/issues/44
Attribute value not directly accessible from server exporting the forwarded attribute (Need to do a read own attribute using DeviceProxy on itself)

## Slide 27: TANGO 9 New Features: Forwarded Attributes
https://github.com/tango-controls/ForwardedComposer

## Slide 28: TANGO 9 New Features: Pipes
Pipes = new way to communicate between client and device
Transports in one call, data with different types
The pipe transports a blob (Tango::DevicePipeBlob)

## Slide 29: TANGO 9 New Features: Pipes
The pipe transports a blobs (Tango::DevicePipeBlob).
The transported blob structure could change at each call.
A blob is defined by a name and a sequence of Tango::DataElement
A DataElement is defined by a name and a piece of data.
data = of a Tango data type or a blob.

## Slide 30: TANGO 9 New Features: Pipes
The transported blob structure could change at each call.
A blob is defined by a name and a sequence of Tango::DataElement
A DataElement is defined by a name and a piece of data.
data = of a Tango data type or a blob.

## Slide 31: TANGO 9 New Features: Pipes

## Slide 32: TANGO 9 New Features: Pipes

## Slide 33: TANGO 9 New Features: Pipes

## Slide 34: TANGO 9 New Features: Pipes
1 DevicePipe dp = mydev.read_pipe("MyPipe");
2
3 DevLong dl;
4 vector<double> v_db;
5 DevVarUShortArray *dvush = new DevVarUShortArray();
6
7 dp >> dl >> v_db >> dvush;
8
9 delete dvush;
Client side: Extracting data with prior content knowledge:

## Slide 35: TANGO 9 New Features: Pipes: Client side: Extracting data with prior content knowledge
1 DevicePipe dp = mydev.read_pipe("MyPipe");
2 size_t nb_de = dp.get_data_elt_nb();
3 for (size_t loop = 0;loop < nb_de;loop++) {
5 int data_type = dp.get_data_elt_type(loop);
6 string de_name = dp.get_data_elt_name(loop);
7 switch(data_type) {
9 case DEV_LONG:
10 {
11 DevLong lg;
12 dp >> lg;
13 }
14 break;
15 case DEVVAR_DOUBLEARRAY:
16 {
17 vector<double> v_db;
18 dp >> v_db;
19 }
20 break;
23 ....
24 } ...
26 }

## Slide 36: TANGO 9 New Features: Pipes
1 DevicePipe dp("MyPipe");
2
3 vector<string> de_names {"FirstDE","SecondDE","ThirdDE"};
4 db.set_data_elt_names(de_names);
5
6 DevLong dl = 666;
7 vector<double> v_db = {1.11,2.22};
8 unsigned short *array = new unsigned short [100];
9 DevVarUShortArray *dvush = create_DevVarUShortArray(array,100);
10
11 dp["SecondDE"] << v_db;
12 dp["FirstDE"] << dl;
dp["ThirdDE"] << dvush;
mydev.write_pipe(dp);
Client side: writing a pipe (2nd Method)

## Slide 37: TANGO 9 New Features: Dynamic commands

## Slide 38: TANGO 9 New Features: Dynamic commands

## Slide 39: TANGO 9 New Features: DEVICE INTERFACE CHANGE EVENT
Special Event to be notified when the device interface changes
  when attribute(s) added/removed
  When command(s) added/removed
Linked to a device (not attribute)
The event is sent after a small delay (50 mS) to eliminate the risk of events storm in case several attributes/commands are added/removed in a loop
Same structure as when requesting the device interface from the admin device + a boolean flag used to warn that their might be no change in the interface (Device was restarted or event reconnection occurred)

## Slide 40: TANGO 9 New Features: DEVICE INTERFACE CHANGE EVENT
void MyCallBack::push_event(Tango::DevIntrChangeEventData *ev)
{
cout << “device interface change event received" << endl;
cout << "Device name = " << ev->device_name << endl;
if (ev->err == true)
cout << "The att change event is an error" << endl;
else {
if (ev->dev_started == true)
cout << "Device has been started" << endl;
cout << ev->cmd_list.size() << " commands" << endl;
for (const auto &elem:ev->cmd_list)
cout << "Command name = " << elem.cmd_name << endl;
cout << ev->att_list.size() << " attributes" << endl;
for (const auto &elem:ev->att_list)
cout << " Attribute name = " << elem.name << endl;
}
}

## Slide 41: TANGO 9 New Features: Pipe events
Used when the user want to push data through a pipe
Sent by user code by using a specific DeviceImpl::push_pipe_event() method
There is no way to ask the Tango kernel to automatically push this kind of event.

## Slide 42: TANGO 9 New Features: Polling threads improvements
Goal: limit the famous error ''Polling thread is late'' when event system used
2 improvements:
  When attributes belong to same device and are polled at same frequency, Replace read_attribute by read_attributes in the polling thread
    Pro: Improve the efficiency (only one call to read_attr_hardware())
    Con: Diagnostic on attribute execution time lost
  Do not send error if thread is late just once

## Slide 43: New Features: DBBench

## Slide 44: New Features: DBBench

## Slide 45: Documentation
http://tango-controls.readthedocs.io

## Slide 46: documentation
1st Tango write-the-doc camp
–
May 2017
Photos: Olga Merkulova - Lukasz Zytniak

## Slide 47: Roadmap #2: Move to Git
Sourceforge / subversion
Github / git
http://sourceforge.net/projects/tango-cs/
https://github.com/tango-controls

## Slide 48: Roadmap #2: Move to Git
Codecov
3rd party tools for free!

## Slide 49: Roadmap #2: Move to Git
Pull Requests
Source: https://medium.com/@swinkler/git-workflow-explained-a-step-by-step-guide-83c1c9247f03
Push

## Slide 50: Roadmap #2: Move to Git
Pull Requests

## Slide 51: LabVIEW binding
https://github.com/tango-controls/labview-binding

## Slide 52: Roadmap #12: Auto-generate Unit Tests
POGO to generate unit tests automatically

## Slide 53: Roadmap #12: Auto-generate Unit Tests

## Slide 54: Roadmap #12: Auto-generate Unit Tests
JTango Maven archetype
Simple Unit tests

## Slide 55: Roadmap #12: Auto-generate Unit Tests

## Slide 56: Roadmap #14: Replace Boost.Python
Replace Boost.Python in PyTango with a lighter weight solution
https://github.com/pybind/pybind11
Proof of Concept tests in progress

## Slide 57: C++ Tango library status
Code restructured
Autotools
Continuous integration with Travis CI, using docker containers
Continuous integration with AppVeyor for Windows
Bug fixes
New features:
    DevEnum labels for DevEnum command parameters
    DevPipeBlob in command parameters
    Tango 10 frequent development releases to Bintray (www.bintray.com/tango-controls) as Debian packages for Tango
    Major releases packaging will go to official repositories

## Slide 58: C++ Tango library status

## Slide 59: JTango status
Code restructured
Bug fixes
Mavenization
Automatic deployment on Bintray
www.bintray.com/tango-controls

## Slide 60: JTango status
Soon on Maven Central

## Slide 61: PyTango status
News since latest ICALEPCS
PyTango 9.2.2 released in September 2017:
  Pipes
  Dynamic commands
  Forwarded Attributes
  Mandatory properties
  Interface Change Events
2 modules for unit-testing added
Bug fixes
Code refactoring
More Unit Tests
Code quality check with pylint and flake8
official tango-controls conda channel
https://github.com/tango-controls/pytango

## Slide 62: Roadmap #3: Remove CORBA completely
  Introduce an abstract transport layer
  Replace CORBA as synchronous communications protocol with a pluggable protocol layer
  remove all dependencies on CORBA
      serialisation library
      data types
  use as first implementation

## Slide 63: Roadmap #3: Remove CORBA completely
cppTango (C++ Tango library):
Code restructured
CORBA notifd events related code purged in Tango V10
Proof of concept refactoring to:
      Isolate CORBA code
      Implement DevVarDoubleArray type using an architecture allowing plugins
      Replace omni_threads with C++ 11 threads
    Compatibility will be preserved all along the way!
      Runtime compatibility
      Source code compatibility with minor changes
      Setup CI for cross-version checking
IMPORTANT

## Slide 64: Roadmap #10 Long Term Support
Provide upgrades for older versions
Long Term Support for Tango 9 (min 5 years after 1st Tango V10 stable release)
  Bug fixes
  Simple new features
tango-9-lts branch on Github: https://github.com/tango-controls/cppTango/tree/tango-9-lts

## Slide 65: Conclusion
Photo: Albert Gea / Reuters

## Slide 66
Many thanks to the TANGO Controls community and kernel team! Thank you for your attention!
Questions?
www.tango-controls.org