## Slide 1: SOLEIL Status
Raphaël GIRARDOT, TangoMeeting 2025

## Slide 2: Outline
SOLEIL II status (upgrade plans)
Current usage of our Web applications
Archiving status at SOLEIL
Taurus usage at SOLEIL
Highlights
Ongoing developments and solutions

## Slide 3: SOLEIL II status (upgrade plans)

## Slide 4: SOLEIL II status (upgrade plans)
SOLEIL Sychrotron
French installation, near Paris
29 beamlines
Opened to external users since 2008
Energy from far IR to hard X-rays
Storage ring 354m, 2.75GeV
~ 450 staff members / ~ 30 computing & electronics

## Slide 5: SOLEIL II status (upgrade plans)
Towards SOLEIL II
  New booster
  New storage ring
10 µm
SOLEIL II
SOLEIL
Beam sizes
400 µm
Emittance < 100 pm.rad.
Brightness
SOLEIL
SOLEIL II
https://www.synchrotron-soleil.fr/en/future-soleil-soleil-ii-project
Budget
Machine parameters
Infrastructure & buildings
Beamlines implementation
Project organization
Phase 1: Construction
Phase 2: Towards full performance
New machine assembly
Shutdown and installation
Restart of 7/10 upgraded + 19/22 adapted beamlines
New machine commissioning
Instrumentation R&D
Beamlines optimisation and upgrade
Laboratories modernization
Instrumentation R&D
Dark period

## Slide 6: Current usage of our Web applications

## Slide 7: Current usage of our Web applications
Grafana for accelerators in production and highly used
  74 users (accelerator operation groups), 144 dashboards
  Based on archiving system for accelerators (GraphQL API)
  Deployed with docker swarm and Portainer
  Still working on monitoring and server scaling

## Slide 8: Current usage of our Web applications
MachineStatusWeb deployed
  Available in restricted networks (private usage)
  Based on archiving system for accelerators (GraphQL API)
  Highly used by operators
  Pending validations from comittees for public usage

## Slide 9: Archiving status at SOLEIL

## Slide 10: Archiving status at SOLEIL
Since 2006
  Intensively used on Accelerators, Beamlines & Labs
  For monitoring and incident analysis
  Complete user autonomy to add new data storage and retrieve data
  Maintaining SOLEIL software stack  Allow smooth migration for users without any downtimes
  Java Tango devices & Java Swing GUIs & Data fetching GraphQL API
  Multiples insertions modes: polling (periodic, change…) & events
2 anomalies detected w/
Local Outlier Factor algorithm for RF systems
Basic use cases study for automatic anomaly (AI) detection based on TANGO archiving data
Improving user experience, by moving from only-desktop GUI to web architecture
  https://gitlab.synchrotron-soleil.fr/software-control-system/tango-controls-archiving
~25 TB since 2006
x5 for SOLEIL II
Before 2024
  Oracle/MySQL Databases
From 2024
Progressive rollout before SOLEIL II’s dark period
  Timescale databases

## Slide 11: Taurus usage at SOLEIL

## Slide 12: Taurus usage at SOLEIL
Taurus is still being tested on 1 beamline.
Simple, but highly used, applications developped.
Various use cases tested.
Taurus looks promising for them, though not perfect yet.
Notes: - Control Helium injection, with automatic stop, as they used to do it with scripting, forgetting to close valve because of the logs invading the script console.
- Diffractometer config switch

## Slide 13: Taurus usage at SOLEIL
Still being tested in control room.
Applications regularly used, some migrated from LabView.
Taurus is highly appreciated
Notes: Perte faisceau (checklist), FBT killer (tuer propre faisceau), interlocks

## Slide 14: Taurus usage at SOLEIL
Taurus releases are regularly checked by our software team.
Keep Taurus team informed of encountered issues and potential solutions.
POC application for a new need on a beamline.

## Slide 15: Highlights

## Slide 16: Highlights
JTango 10 RC 1 is now available!
  jtango-10 branch https://gitlab.com/tango-controls/JTango/-/tree/jtango-10
  Soon available in maven
C++ software factory migrated to Conan/Cmake
  All of our C++ devices (400) are built with Conan (delivered in production)
  Ready for seamless upgrades

## Slide 17: Ongoing developments and solutions

## Slide 18: Ongoing developments and solutions
Working on alternatives to Java for UI
  More web
  More python
Upgrade from Tango 9.2.5 to latest LTS
  Is Tango 10 LTS, or soon LTS?
Migration from Java 8 to latest LTS
Migrating Database device:
  from 5.4 to 5.22
  from MySQL 5.6 to MariaDB 10.5