## Slide 1: ICA Activities Status – Tango Meeting 2020 November
Sandra PIERRE-JOSEPH ZEPHIR

## Slide 2: Plan
SOLEIL and Tango
ICA Team
  Its members
  Its activities
  Pepper by SOLEIL Upgrade subjects
  Toward further collaborations …
U

## Slide 3: Synchrotron SOLEIL
Third Generation Synchrotron Radiation Facility (https://www.synchrotron-soleil.fr)
SOLEIL’s nominal energy is 2.75 GeV - storage ring with a circumference of 354 m (Accelerators called Machine)
Electrons trajectory is bent by magnetic fields => emission of light in an extremely thin beam.
29 Beamlines to explore the matter
Upgrade is in progress (to 4G), Conceptual Design Report is being written
Some goals to achieve before the beginning of the shutdown (in 2 or 3 years)
U

## Slide 4: SOLEIL and TANGO
In the collaboration since the beginning
Full Tango installation (Machine and Beamlines) – V9.2.5
Jive, Astor, AtkPanel, Devices : essential tools well known by 2/3 of SOLEIL’s employees !
 Next SOLEIL generation based on next Tango generation 
U

## Slide 5: ICA team … and TANGO
ICA Team in charge of providing control command system software for SOLEIL’s Machine, Beamlines and Laboratories.
Leaving from ICA Team
  Katy Saintin – near 3 years ago – CEA (Public French Research Center)
  Gregory Viguier - one and half year ago – Canada
  Jean Coquet – near 4 years ago – IA on SOLEIL beamline
  Majid Ounsy - one year ago – SOLEIL Data analysis group (GRADES)
  Nicolas Leclercq - one and half year ago - SOLEIL Information System Strategy
  Alain Buteau - one year ago – head of SOLEIL IT group
Now 10 Permanents (of 350), 1 Apprentice, 1 Machine operator at 20%, Contractors

## Slide 6: ICA team … and TANGO
  Same TANGO distribution in all control systems
  Some applications are developed by Machine/Beamlines persons
Implication in the collaboration
  Java Archiving system HDB/TDB/SNAP
  JTangoServer
  Tango V10 Specification redaction
  LabView, Matlab, Igor Binding => Still Nicolas – on collaborative way by the help of pull-requests on github

## Slide 7: Tango Devices
Tango Devices In number
  Near 450 distincts Dservers type to pilote equipments, to process data
 | TANGO STATS – 09/2020 |  | 
 | DEVICES_NUMBER | DSERVER_DEFINED | TANGO_HOSTS_NUMBER
MACHINE | 15805 | 5073 | 233
BEAMLINES | 20330 | 5703 | 366
LABORATORIES | 6634 | 1384 | 87
C++
JAVA
1 contractor

## Slide 8: Lima Detector
Collaboration with ESRF, also used by Alba, MaxIV, Desy
Windows- Linux 32-bit and 64-bit
One kind of DServer and lot of specifics devices :
  AndorCCD BaslerCCD Dhyana Eiger Hamamatsu ImXpad Lambda MarCCD Maxipix Merlin Pco PerkinElmer PilatusPixelDetector PrincetonCCD ProsilicaCCD SimulatorCCD SlsEiger SlsJungfrau SpectrumOneCCD (WIP) SpectralInstrument (WIP) UFX Uview XpadPixelDetector Xspress3
1 contractor

## Slide 9: Acquisition Service and Data storage
2 Acquisition services
  Step by Step and FlyScan
  With electronic team
Experimental Data Files Management
  See next presentation
IHM
IHM

## Slide 10: User Interfaces
Command Line Spyc in Python, IPython
  Used by 8 Beamlines
  Generics commands (move, scan …) + Beamlines specifics commands developed by themselves
Graphical provided in JAVA-Swing
  Sequencer tool Passerelle (SupportSquare)
  Scada tool named Coox (Ordinal Software)
  Various IHM

## Slide 11: User Interface
Toward Web Applications
  Old Rest API available upper Archiving Service:
    Client MamboWeb
    Some applications for accelerators people developped
  First implementation of Archiving API in GraphQL
  First implementation of Grafana plugin upper Rest API
  WebJive installation on development plateform

## Slide 12: Archiving Service
HDB/TDB/SNAP on Oracle DB
  Polling, beginning of archiving events usage (configuration and monitoring must be improved)
  Machine, Beamlines, Laboratories
  Upgrade projection: study other kind of DB, other way to store data, analyse others Tango collaboration solutions
PANIC – alarms tool
  Tested by Machine people / In a near future to be deployed in production
  Beamlines people are also interested
IHM
Jérémy
Oracle DBA
U

## Slide 13: Tools
CI/CD
  CI and automatic Delivery
  Jenkins / Maven for C++ and Java
  Windows 32/Linux
  Aging installation
  Toward Conan/Cmake
  SVN, CVS => Git
  Be able to be evolutive and strong Software factory for Upgrade
Jira (Bug Traker) /Confluence (Collaborative tool)
  Confluence management is moving toward another group
  Toward an OnCloud installation
U

## Slide 14: Tools
Testing
  Lot of Unitary Tests in Java devices automatically executed in CI plateform
  UT on unitary graphicals components not included in the CI plateform
  No automatics tests at device C++ level – some python tools has been created to mock systems has a socket server, to trigger tests => improve
  One testing plateform in simulated env before delivery but lot of devices are tested on production during testing slot
  Upgrade : having automatic tests, creation of a plateform with somes real equipements, developpement of simulators …
  Tango Workshop to discuss about our various practices?
U

## Slide 15: Operation
On-Call duty period => Need tools to be more confortable
Log files exploitation
  ElasticSearch is being studied
One Tango DB per Beamline => In need of a tool to collect data to be able to explore them (find where a class of device is used, the various configuration …)

## Slide 16: Infrastructure
For the Control Systems
  Machine – Beamlines - Laboratories
  Physical and Virtuals Machines – Proxmox – CentOs6
  Windows Images (CompactPCi are managed by Electronic group)
  5 Automatic deployments per year
  Tango DB Management
  …
 | INFRA STATS – 09/2020 | 
 | HN_NUMBER | CT_NUMBER
MACHINE | 22 | 258
BEAMLINES | 63 | 290
LABORATORIES | 12 | 94
HN_NUMBER = Number of physical servers in production
CT_NUMBER = Number of virtuals conteneurs

## Slide 17: Our Names
Sandra PIERRE-JOSEPH - Gwenaëlle ABEILLE - Stéphane POIRIER
Jade PHAM – Raphaël GIRARDOT – Arafat NOUREDDINE
Stéphane LE – Patrick MADELA – Xavier ELATTAOUI – Florent LANGLOIS
Thomas MARION – Antonin HOTTOIS
Email : firstname.famillyname@synchrotron-soleil.fr

## Slide 18: In Image
One permanent contract here : https://www.synchrotron-soleil.fr/fr/emplois/ingenieure-developpement-c
  2 missions: C++ developer / Project management assistant