## Slide 1
Apollon Control System Status
Stéphane Marchand
Laboratoire pour l’Utilisation des Lasers Intenses
Tango meeting 2023-06-27

## Slide 2: Overview
Facility
Team
Key figures
Network improvements
Tango system, diagnostics
Archiving system
Summary

## Slide 3: Localization, Apollon building
LULI (High intensity laser laboratory); site : “L’Orme des Merisiers” (25km from Paris, 5km from X) but also 2 facilities on X campus (LULI2000 & HERA, Tango too)
Underground
Heavy shielded installation
Laser : 700 m2 (cleanroom)
Exp1 (long focal) : 420 m2
Exp2 (short focal) : 210 m2
Control rooms : 200 m2
Workshops : 480 m2
Offices : 300 m2

## Slide 4: Inside Apollon
Long focal Area (420 m2)
Control room
Compression and switchyard laser subsystem
<link for a 3D Virtual tour>
Short Focal Area (210 m2)

## Slide 5: Milestones
Reappointment of the French nuclear safety authority (ASN) authorization until the end of 2027
Third year in operation : > 10 experimental campaigns
2023: main laser beam (40cm diam.) commissioned
  Two beams in operation : 1PW and multiPW
  First qualification multiPW experiment in Short Focal Area w/ more than 2PW on target, on the multiPW roadmap (2024: 4PW; 2025: 8PW)

## Slide 6: Command-Control Team (C2S)
(currently playing w/ Tango)
Jean-Luc Bruneau
Laurent Ennelin permanent positions
Stéphane Marchand
Maguette Sow, 2nd year Engineer apprentice (until mid-2024)
Sonia Minolli (since end of 2021 as service w/ Nexeya then fixed-term contract w/ LULI) who came with super-strong quality code skills

## Slide 7: Key figures
Devices in operation | April 2019 | April 2021 | December 2022 | Updated Estimation
Hypervisors | 7 | 7 | 6 | <8
Virtual Machines | 33 | 49 | 54 | 60
Control stations | 18 | 41 | 43 | ~50
CCD: laser beam CCD: plasma diag CCD: live exp. setup | 42 | 59 12 8 | 62 12 8 | ~80 12(*) 8(*)
Calorimeters | 16 | 18 | 19 | >20
Motor channels: laser Motor interaction chamber Motor: diagnostics | 66 | 93 25 ~15 | 100 ~50(*) 20 | 120 ~60(*) 30
Delay generators | 10 | 12 | 12 | ~14
* : Depending on campaigns

## Slide 8: 2021 Network and VM Upgrades
2 cores <=> 4 x 25Mbps
10Gbps Redundancies
LULI @EP

## Slide 9: Network separation
In short: redundancy 10-Gbps everywhere w/ separation of cameras' flux
2515
…
…
…
…
VM
server
C2S
VMware v6.0.0
~80 VM
Updated from "office software" version w/o any redundancy from 2015 (see extra slide)

## Slide 10: Versions
C2S Devices | Vacuum Devices (Soleil)
64-bit Windows 10 Python 3.8 Tango 9 PyTango 9 NI LabView 2022 Currently updating to 64-bit Windows Server 2022 Datacenter on vSphere web client | 64-bit Linux Ubuntu 14.04 LTS 6 Tango 9 NI LabView 2016
Archiving | GUI
Linux Ubuntu 20.04 LTS Tango 9.3.4 HDB++: Devices version 2.0.0, GUI Configurator version 3.1.1 BDD: MySQL | Windows 7 32 bits Python 2.7 Tango 8 PyTango 8 PyQt 4.8 Currently updating as C2S Devices servers

## Slide 11: GUI for monitoring
Cameras
Motors
Vacuum
Personal Security System

## Slide 12: Laser diagnostics web interface
NOW: PHP to shared filesystem resource
upgrading to
NEXT: Django to Archiving Database

## Slide 13: Vacuum analysis w/ current archiving mode
Vacuum chief leader: Jean-Philippe Delaneau

## Slide 14: Infrastructure for Archiving
VM arc
ArcSync
Communication w/ synchros
VM servers: Spectrum, Energy, Vacuum…
Tango Devices servers
hdb++[es|cm]
Archiving Devices
VM hdbpp
MySQL Database
VM bdd?
Web service
Python
Data extraction from Database
Emit soft top_shot
Emit archive_event
OR BDD ON VM?
Shared resource
Filesystem
Copy in
csv-like file
MySQL Database
VM bdd

## Slide 15: Status for HDB++ Archiving
Laserbeam (from pilot to experimental rooms) at different frequencies: F1 (10Hz), F2 (1Hz), F3 (10sec), F4 (1min); shots at F4 (1min) rate
Different modes of archiving | 
Continuous (long term monitoring F2—F4) Tango polling (ie. ~150 attributes for vacuum system at F2 rate) | Sequence (trigged on shots during campaigns, F4: laser and experimental diags)
Trigged (short duration period, F3—F4) is synchronized w/ F1 signal | 
Well, under construction, still some major issues (timeout, lost database connection, Faulty attributes) BUT we're back at it, at least.

## Slide 16: Summary
Network and virtualized system upgraded last year
VM environment upgrades within summer
Tango system widely used (Apollon but also LULI2000 and Hera, 3 facilities of LULI)
Python3, PyQt5 upgrades (devices/GUI)
HDB++ Data archiving solutions in progress

## Slide 17: Thank you for your attention!

## Slide 18: Global DS monitoring

## Slide 19: Apollon network: 2018