## Slide 1: Archiving Sardana elements
Dmitry Egorov
40th Tango Community meeting
Jun 8 – 12, 2026
ALBA Synchrotron

## Slide 2
Sardana (heavily simplified) structure
Motor Z
Device: motor/ctrl/3
Motor Y
Device: motor/ctrl/2
Motor X
Device: motor/ctrl/1
Pool device
Device: ctrl_sys/Pool/1
MotorController class source file
Controller logic:
Hardware connection, configuration, etc.
Axes logic:
Mapping values and commands to channels - position, limits, state, stop(), etc.
Dynamically loaded packages
Motor Controller
Device: controller/motor_ctrl/1
Sardana Device Server
Motor XYZ
Device: motor/ctrl/123
…
Init Controller device with SardanaDevice structure
(dynamic attributes, commands)
Sardana elements
belong to Controller

## Slide 3
Tango attributes read
Motor Z
Device: motor/ctrl/3
Motor Y
Device: motor/ctrl/2
Motor X
Device: motor/ctrl/1
Position attribute
polling
MotorController class source file
Controller logic:
Hardware connection, configuration, etc.
Axes logic:
Mapping values and commands to channels - position, limits, state, stop, etc
read_position()
Get position value
Check state value
Other
Sardana
“magic”
read_position()
Get position value
Check state value
Other
Sardana
“magic”
read_position()
Get position value
Check state value
Other
Sardana
“magic”
Hardware communication
Read_attribute() * N

## Slide 4
Tango attributes read (during a scan)
Hardware communication
Absolute scan for specified motor:
ascan motor_x 0 10 10 0.1
<motor> <start_pos> <final_pos> <nr_interv> <integ_time>
All motors polling
…
PyDs_PythonError: Exception: Cannot move: already in motion
Hint: in Spock execute `www` to get more details
motor_x
1
motor_x
2
Motion failed due to: DevFailed[
DevError[
desc = Exception: Cannot move: already in motion

## Slide 5
Queuing issues…
It’s difficult to control priorities or sort the queue with requests from different devices

## Slide 6
Queuing issues…
…

## Slide 7
How can we read values in batches?
Motor Z
Device: motor/ctrl/3
Motor Y
Device: motor/ctrl/2
Motor X
Device: motor/ctrl/1
MotorController class source file
Controller logic:
Hardware connection, configuration, etc.
Axes logic:
Mapping values and commands to channels - position, limits, state, stop, etc
Motor Controller
Device: controller/motor_ctrl/1
Get all
positions
Push updated values
cmd ?FPOS [register] addr [addr … ] → value [value … ]
Returns the positions for the specified axes.
The ?FPOS query is intended to be used for frequent polling from the control host

## Slide 8
IcePAP Sardana controller modifications
MotorController class source file
Controller logic:
Hardware connection, configuration, etc.
Axes logic:
Mapping values and commands to channels - position, limits, state, stop, etc
New properties to configure which axes to read
Controller attributes to poll them to read data from hardware
“Read_attribute” creates background thread to not lock the polling thread
Background thread updates Dial Position (if motor is not Moving)

## Slide 9
IcePAP Sardana controller modifications
Polling Status
Polled attribute name = HighUsagePositions
Polling period (mS) = 5000
Polling ring buffer depth = 10
Time needed for the last attribute reading (mS) = 0.492
Data not updated since 2 S and 886 mS
Delta between last records (in mS) = 5000, 5000, 4994, 5005
Polled attribute name = LowUsagePositions
Polling period (mS) = 60000
Polling ring buffer depth = 10
Time needed for the last attribute reading (mS) = 14.662
Data not updated since 44 S and 875 mS
Delta between last records (in mS) = 60010, 59984, 60019, 59999
Polled attribute name = MediumUsagePositions
Polling period (mS) = 10000
Polling ring buffer depth = 10
Time needed for the last attribute reading (mS) = 1.183
Data not updated since 4 S and 997 mS
Delta between last records (in mS) = 10009, 10007, 10000, 9990
New polled attributes to query data
New properties with lists of axes
Code modifications are in the end of presentation
https://gitlab.com/dmiego/sardana/-/tree/motor-archiving
https://gitlab.com/dmiego/sardana-icepap/-/tree/motor-archiving

## Slide 10
Subscribe to archiving events
EventData[
attr_name = 'tango://b-v-veritas-csdb-0.maxiv.lu.se:10000/b316a-o02/opt/mono-01-m2pit/position'
attr_value = DeviceAttribute(data_format = tango._tango.AttrDataFormat.SCALAR, dim_x = 1, dim_y = 0, has_failed = False, is_empty = False, name = 'position', nb_read = 1, nb_written = 1, quality = tango._tango.AttrQuality.ATTR_VALID, r_dimension = AttributeDimension(dim_x = 1, dim_y = 0), time = TimeVal(tv_nsec = 0, tv_sec = 1780661934, tv_usec = 101238), type = tango._tango.CmdArgType.DevDouble, value = 3.0446556158196554, w_dim_x = 1, w_dim_y = 0, w_dimension = AttributeDimension(dim_x = 1, dim_y = 0), w_value = 3.0446494033420493)
device = Motor(b316a-o02/opt/mono-01-m2pit)
err = False
errors = ()
event = 'archive'
reception_date = TimeVal(tv_nsec = 819, tv_sec = 1780661934, tv_usec = 103010)]
EventData[
attr_name = 'tango://b-v-veritas-csdb-0.maxiv.lu.se:10000/pm/mono_energy_calib_ctrl/1/position'
attr_value = DeviceAttribute(data_format = tango._tango.AttrDataFormat.SCALAR, dim_x = 1, dim_y = 0, has_failed = False, is_empty = False, name = 'Position', nb_read = 1, nb_written = 1, quality = tango._tango.AttrQuality.ATTR_VALID, r_dimension = AttributeDimension(dim_x = 1, dim_y = 0), time = TimeVal(tv_nsec = 0, tv_sec = 1780662392, tv_usec = 806433), type = tango._tango.CmdArgType.DevDouble, value = 576.5995760672288, w_dim_x = 1, w_dim_y = 0, w_dimension = AttributeDimension(dim_x = 1, dim_y = 0), w_value = 576.6000000000165)
device = PseudoMotor(pm/mono_energy_calib_ctrl/1)
err = False
errors = ()
event = 'archive'
reception_date = TimeVal(tv_nsec = 903, tv_sec = 1780662392, tv_usec = 808568)]
Physical motor
PseudoMotor

## Slide 11
How It Has Already Helped
Green and yellow – physical motors positions, blue – pseudomotor position,
Orange and red – physical motors states

## Slide 12
How It Has Already Helped
Target positions are reached
One of the motors is still busy
Green and yellow – physical motors positions, blue – pseudomotor position,
Orange and red regions – physical motors states

## Slide 13
How It Has Already Helped
Before tuning
After tuning

## Slide 14
Grafana dashboard

## Slide 15
Bonus: a naive attempt to add aliases to the HDB++
SELECT
data_time AS "time",
value_r as "$Motor",
value_w as "${Motor}_write"
FROM att_scalar_devdouble
WHERE
$__timeFilter(data_time)
AND
att_conf_id = (select att_conf_id from att_alias where alias = '$Motor')
ORDER BY data_time

## Slide 16: Thank you!

## Slide 17
Sardana and IcePAP controller modifications
def ctrl_event(self, ev_src, ev_type, ev_val):
if ev_type.name == "init_attribute_values":
axis, axis_name = ev_val, self.GetAxisName(ev_val)
self._elements[axis] = self.pool_ctrl.get_element(axis=axis)
self._check_if_archived(axis, axis_name, self.attributes[axis]['use_encoder_source'])
def _check_if_archived(self, axis_id, axis_name, use_enc_source):
if use_enc_source:
if axis_name in self.HighUsageAxes:
self.archived_enc_axes["high_usage"].add(axis_id)
def init_attribute_values(self, attr_values: Optional[Dict[str, Any]] = None) -> None:
"""Initialize attributes with (default) values. """
………
self.controller.fire_event(EventType("init_attribute_values"), self._axis)
sardana/pool/poolelement.py
sardana_icepap/ctrl/IcePAPCtrl.py
Notify listeners when element attributes are initialized and values are assigned
Listen to “init attributes” event to check if axis is archived
Sort axes by “type” and encoder usage

## Slide 18
IcePAP controller modifications
def getHighUsagePositions(self):
return self.readPositions(self.archived_enc_axes["high_usage"])
def readPositions(self, axes_to_read):
for chunk in self.divide_by_chunks(axes_to_read):
if chunk:
t = threading.Thread(target=self.read_in_background, args=(chunk, "MEASURE"))
t.start()
return str({axis: self.attributes[axis]['position_value'] for axis in axes_to_read})
sardana_icepap/ctrl/IcePAPCtrl.py
“read_attribute” function
Split list of axes to batches and read them in background thread
The original list is split up to ensure that each request to the hardware takes less than 10 ms, which is the Sardana scan reading interval.

## Slide 19
Sardana modifications
sardana_icepap/ctrl/IcePAPCtrl.py
“read_attribute” function
def read_in_background(self, axes, register):
ans = self.ipap.get_fpos(
axes,
register=register
)
for axis, value in zip(axes, ans):
eval_globals = numpy.__dict__
spu = float(self.attributes[axis]['step_per_unit'])
eval_locals = {'VALUE': value, 'value': value,
'SPU': spu, 'spu': spu}
enc_src_formula = self.attributes[axis]['encoder_source_formula']
dial_pos = eval(enc_src_formula,
eval_globals,
eval_locals)
self.attributes[axis]['position_value'] = float(dial_pos)
last_state_value = self.attributes[axis]["last_state_value"]
# if axis is Moving - it's managed by PoolMotion
# we don't want to push data from here, because it comes from another thread
# it might come later and has old value, which can be confusing
if last_state_value != State.Moving:
self._elements[axis].put_dial_position(SardanaValue(dial_pos), propagate=2)
Query raw values from hardware
Calculate position from raw values
Push new values to Motor Devices

## Slide 20
Sardana modifications
def initialize_dynamic_attributes(self):
attrs = PoolElementDevice.initialize_dynamic_attributes(self)
……
self.set_archive_event("position", True, True)
self.set_archive_event("state", True, True)
sardana/tango/pool/Motor.py + sardana/tango/pool/PseudoMotor.py
Configure devices to push archive events from code
sardana/tango/core/SardanaDevice.py
put_dial_position() triggers _set_attribute_push(), which already pushes change events
def _set_attribute_push(self, attr, value=None, w_value=None, timestamp=None,
quality=None, error=None, priority=1):
……
args = attr_name, value, timestamp, quality
self.push_change_event(*args)
if attr_name == 'position':
self.push_archive_event(*args)